## Slide 1: Case Study: CPU Meltdown Exploit 2018

## Slide 2: Disclaimer
The entities affected by the cyber breach have not disclosed all details of the incident publicly and likely will not do so in the future. However, sufficient information is available online and within the cybersecurity community to infer the probable events during the breach.
While efforts have been made to ensure the accuracy of the information provided, the presenter assumes no responsibility for its accuracy or for the consequences of its use.

## Slide 3: Sources of Information
This case study is adapted from the 2018 CPU Meltdown vulnerability, utilizing information from public sources and modified for educational purposes.
For further details, please refer to the additional resource provided in this presentation.

## Slide 4: Readme Information
Target audience: Undergraduate, Graduate.
Keywords: Hardware security, Zero-day vulnerability, side channel attacks
Last updated: May 1, 2024

## Slide 5: Learning Objectives
Describe the CPU Meltdown Vulnerability from 2018
Explain Zero-Day Vulnerability
Explain side-channel attacks

## Slide 6: Background
Meltdown was independently discovered and reported by three teams in June 2017: Jann Horn (Google Project Zero), Werner Haas, Thomas Prescher (Cyberus Technology), Daniel Gruss, Moritz Lipp, Stefan Mangard, Michael Schwarz (Graz University of Technology)
Meltdown takes advantage of a CPU design “flaw” Allows any program to read sensitive information in memory Unpriveledged user, reading arbitrary memory - including kernel memory
There is a similar but more complex Spectre exploit. We won’t cover it here.
Source: https://en.wikipedia.org/wiki/Meltdown_(security_vulnerability)

## Slide 7: What is Side-Channel Attack?
An attack that derives information from a non-direct or unintentional information source. Sources can include sound, vibration, electromagnetic emissions.
Examples:
Acoustic cryptanalysis -Sounds of keys clicking can be analyzed and typed phrases and passwords can be recovered -Supersonic sounds directed at an accelerometer to alter readings or ultrasound to attack Siri
Electromagnetic emissions -It is well known that old style CRT monitors generate a lot of EM emissions, and it has been shown that those emissions can be collected at a distance and then used to reconstruct information that is being displayed on the original screen

## Slide 8: Modern CPU
Modern computers (including CPU and OS) try to ensure that a user program can not randomly access other user’s memory or data without authorization and authentication.
Modern CPU has built-in security mechanism to supprt that, and it works very well, until the meltdown exploit…
Modern CPU has internal cache, it is much faster than main PC memory RAM.
Modern CPU use out-of-order exectuion to speed up performance.

## Slide 9: Out-of-order execution
Instead of stalling the execution, modern processors run operations out-of-order i.e., they look ahead and schedule subsequent operations to idle execution units of the processor.
Source: https://en.wikipedia.org/wiki/Out-of-order_execution

## Slide 10: Speculative execution
Speculative execution
CPU guesses what the outcome of execution will be, and then executes subsequent steps in the background.
CPU Cache memory stores data that it is working with.
CPU copies info from main memory and stores it in cache.
Main memory - protected area stores sensitive info
  CPU protects this memory from being read
Protection is not honored during speculative execution
CPU speculates and executes
  if correct speculation branch, then stored in cache

## Slide 11: Speculative execution
Speculative execution
Software tries to compare protected memory item (password) to some letter “P”.
  If it returns true it will be in the CPU cache memory and return fast.
  If not, then it will return from main memory and be return slow.
Then just check the result timings fast is true, slow is false.

## Slide 12: Technical details of Meltdown
Security is based on separating Kernel memory address ranges that are not accessible by user space
Meltdown allows non-privileged user to read Kernel memory space
Meltdown takes advantage of out of order execution - speculative execution
  The malicious software clears the CPU cache memory
  The malicious software makes a request to read kernel memory which is illegal because it is protected
  The malicious software makes a second request to conditionally read a VALID memory location if the first (and illegal) request contains a certain value
  With speculative execution - BOTH requests are executed before both requests are denied because of illegal out of bounds memory.
  Because both requests are denied, results are not returned. However because of speculative execution both requests were processed, and the accessed memory locations are stored in CPU cache memory.
Source: https://meltdownattack.com/meltdown.pdf

## Slide 13: An Analogy Using McDonald
McDonald has food such as fry, coke, and hamburger.
(Assuming) Taylor Swift went to McDonald, ordered an hamburger, and left.
A paparazzi guy A behind Taylor Swift told the McDonald’s frontdesk person: “I want to order the same food as that pretty lady”.
The McDonald person said: “Please wait in order, there is one person before you”. But the person in McDonald’s kitchen heard of the order, to SPEED UP future orders, he speculate and made a hamburger and put it on shelf.
Now it is A’s turn for ordering. But, the McDonald’s frontdesk person said: “You can not order like that. It is a violation of privacy.” So A is kicked out of McDonald.
There is another paparazzi guy B behind A. Now B said: “Give me an order of fry, or coke, or hamburger. I am starving. Whichever fastest, please give it to me”.
B got a hamburger.
So paparazzi B know Taylor Swift ordered a hamburger at McDonald.
Hidden Assumption: The paparazzi team need to make sure McDonald’s shelf is empty at the very beginning.

## Slide 14: A more technical explanatory example
Suppose the address at 3000 is not directly readable, and it could have any value from 1 to 5.
A hacker could execute an instruction "Read memory at an address given by (5000 plus the value of memory at address 3000)".
If address 3000 contains 1, then the CPU will try to return the value of memory at address 5001; if address 3000 contains 2 it will try to return the value of memory at address 5002, and so on.
If the hacker executes a timing attack, and it shows that the CPU was slower to read from addresses 5001, 5002, 5003 and 5005, but faster for address 5004.
The hacker can conclude that the reason is that it has cached data from address 5004, and that this is because it has recently accessed that address.
So the hacker can deduce that address 3000 contained the value "4".
Source: https://en.wikipedia.org/wiki/Meltdown_(security_vulnerability)

## Slide 15: Impact
Basically everything
All Intel processors since 1995
  All out-of-order Intel processors released since 1995
  All modern processors that use out-of-order execution
Some ARM processors
AMD chips
  It is unclear if AMD chips are affected.
Desktops
Laptop
Phones
Embedded systems
Source: https://en.wikipedia.org/wiki/Meltdown_(security_vulnerability)

## Slide 16: Impact
Basically everything
Read arbitrary real memory address space
  Allows unprivileged account access to sensitive information
Potential for paravirtualization isolation to be compromised
  Basically allowing a virtual guest to read host memory
  Includes cloud host based systems.
Source: https://en.wikipedia.org/wiki/Meltdown_(security_vulnerability)

## Slide 17: Solution
There are software updates to help mitigate the risk of this particular CPU cache side channel attack
  With performance penalty.
However, this is a hardware issue and can only be truly fixed with a hardware solution.
  Very costly and difficult.
The only real fix is to redesign CPU architecture
Source: https://en.wikipedia.org/wiki/Meltdown_(security_vulnerability)

## Slide 18: Lessons learned
Meltdown exploits a CPU cache side-channel attack to read protected kernel memory
  Basically a privilege escalation
  Provides a dump physical (protected kernel) memory
Virtualization is vulnerable
  Guests could read host shared memory

## Slide 19: This is only the beginning…
More and more CPU/Chip related hardware exploits using side channel attacks are discovered by researchers.
  https://www.cnet.com/news/intel-microsoft-reveal-new-variant-on-spectre-meltdown-chip-security-flaws/
  https://www.crn.com/news/security/300100596/spectre-meltdown-part-two-research-firm-audit-reveals-critical-flaws-backdoors-in-four-amd-processors.htm
  https://www.wired.com/story/speculative-store-bypass-spectre-meltdown-vulnerability/
It becomes a new hot area of research in cybersecurity…

## Slide 20: Discussion Questions
How did the Meltdown vulnerability exploit modern CPU features like out-of-order and speculative execution?
Notes: The Meltdown vulnerability exploits modern CPU features such as out-of-order and speculative execution to access protected memory. Out-of-order execution allows CPUs to execute instructions out of sequence to maximize performance, while speculative execution involves the CPU predicting the path of future operations and executing them ahead of time. Meltdown manipulates speculative execution to access kernel memory that should be off-limits to user programs. By timing the execution and analyzing the CPU cache, an attacker can infer the contents of the protected memory, bypassing traditional security mechanisms that rely on memory isolation between user and kernel space.

## Slide 21: Discussion Questions
What are side-channel attacks, and how do they relate to the Meltdown exploit?
Notes: Side-channel attacks derive sensitive information from indirect sources, such as timing information or electromagnetic emissions, rather than exploiting direct security vulnerabilities. In the case of Meltdown, the attack leverages a side-channel method to infer the contents of kernel memory. By exploiting how speculative execution leaves traces in the CPU cache, Meltdown attackers can measure cache access times to deduce whether specific memory locations were accessed. This indirect method allows the attacker to piece together sensitive information without directly violating memory access restrictions, highlighting the effectiveness of side-channel techniques in circumventing traditional security boundaries.

## Slide 22: Discussion Questions
How can the Meltdown vulnerability be mitigated, and what are the limitations of these mitigation strategies?
Notes: Mitigating the Meltdown vulnerability involves applying software updates such as Kernel Page Table Isolation (KPTI), which separate user and kernel memory spaces more effectively. These patches help to prevent unauthorized access to kernel memory by altering how speculative execution handles protected data. However, these mitigations often result in performance degradation due to the added overhead in memory management. Additionally, since Meltdown exploits fundamental hardware flaws, complete mitigation would ideally require redesigning CPU architectures, which is not feasible for existing hardware, making these software patches a necessary but imperfect solution.

## Slide 23: Discussion Questions
What lessons can be learned from the discovery and handling of the Meltdown vulnerability in terms of hardware security and future research directions?
Notes: The Meltdown vulnerability teaches critical lessons about the importance of integrating security into the design and development of hardware. It reveals that performance optimizations, such as speculative execution, can introduce significant security risks if not carefully managed. The incident underscores the need for ongoing research into hardware security and the development of more robust testing methodologies to identify vulnerabilities early in the design process. Moving forward, collaboration between researchers, industry, and security professionals is essential to anticipate and mitigate potential hardware exploits, ensuring that future CPU designs prioritize both performance and security.

## Slide 24: References and Resources
1. The wiki page: https://en.wikipedia.org/wiki/Meltdown_(security_vulnerability)
2. A short Youtube video: https://www.youtube.com/watch?v=bs0xswK0eZk
3. A technical paper: https://meltdownattack.com/meltdown.pdf
4. A hour-long Youtube video: https://www.youtube.com/watch?v=8FFSQwrLsfE