## Slide 1: Case Study: Pennsylvania Water Breach

## Slide 2: Learning Objectives
Identify the vulnerabilities in this breach
Importance of alarms and monitoring
Understand cyber threats to infrastructure and the risks they posed
Understand Nation state actors

## Slide 3: Overview of Aliquippa Municipal Water
MWAA (Municipal Water Authority of Aliquippa) serves over 6,000 residents of Pennsylvania
Their infrastructure includes 82 miles of water mains, 900 isolation valves, and 450 hydrants, supported by 3 booster stations and 8 pressure regulating valves
Relatively small and its systems are aging

## Slide 4: Aliquippa Municipal Water Attack Summary
On November 25 of 2023, attackers compromised MWAA through a booster station PLC (programmable logic controller) that was exposed to the open internet
MWAA was alerted and took manual control, relied on backup operations to maintain water pressure
The PLC was isolated from the primary water treatment infrastructure which limited the scope of the attack​
Due to MWAA being critical infrastructure, FBI and CISA became involved in investigating the breach and providing support

## Slide 5: Attack Details
The vulnerable PLC was a Unitronics Vision product, responsible for regulating water pressure
Unitronics Vision products have been known to have weak default passwords, and a critical vulnerability had been discovered just months earlier
This vulnerability allows an attacker to store malicious code on the system, which can then be later retrieved by a client and executed
This poor security allowed for attackers to easily compromise the PLC and leave a provocative message on the PLC’s control panel

## Slide 6: Attack Details Cont.
Hacker group from Country A known as “Cyber Av3ngers” claimed responsibility
The company Unitronics was based out of Country B that has tension with Country A
This political motivation lead to Unitronics Vision products being targeted, regardless of their location
Attackers left behind the message: “Every equipment made in Country B is Cyber Av3ngers legal target”

## Slide 7: Nation State Actors
Nation state actors, like Cyber Av3ngers, exploit critical infrastructure systems for political, economic, or strategic goals
By going after infrastructure like wastewater, power grids, or dams, nation state actors can cause significant disruption without having to engage in traditional military conflict
These attacks occur in the “grey zone" – they are not armed conflicts, but not peaceful either, making attribution and retaliation complicated
Cheaper, less effort and risk involved in comparison to armed conflicts

## Slide 8: Reflection & Lessons Learned
ICS (industrial control systems) should not be exposed to the open internet!
Always change default passwords
Have an incident response plan to critical infrastructure breaches
In this case, MWAA was monitoring their systems, and action was quickly taken to disconnect the compromised PLC and minimized the impact
While third party vendors are needed to support critical infrastructure, they can introduce more risk

## Slide 9: References and Resources cont.
International cyber law: interactive toolkit. (2024, September 11). Cyber incident against a Water Authority in Pennsylvania (2023). International cyber law: interactive toolkit. https://cyberlaw.ccdcoe.org/wiki/Cyber_incident_against_a_water_authority_in_Pennsylvania_(2023)#cite_note-5
Kovacs, E. (2023, December 2). Hackers Hijack Industrial Control System at US water utility . SecurityWeek. https://www.securityweek.com/hackers-hijack-industrial-control-system-at-us-water-utility/
Lyngaas, S., & Sgueglia, K. (2023, November 28). Federal officials investigating after pro-iran group allegedly hacked Water Authority in Pennsylvania. CNN. https://www.cnn.com/2023/11/28/us/pennsylvania-water-cyberattack/index.html
Wolfe, J. (2023, November 30). Aliquippa, Pennsylvania suffers cyberattack on Booster Station plc. WaterWorld. https://www.waterworld.com/water-utility-management/article/14302077/aliquippa-pennsylvania-suffers-cyberattack-on-booster-station-plc